## Slide 1: COMP1860 Building our Digital World: Computer Systems & Architecture
S1.W2.L1: Number Systems & Integer Representations
Dr James Dyer

## Slide 3: Learning Outcomes
Explain the bit-level representations of fixed-length numbers.
Translate numerical data from one format to another.

## Slide 4: Text Book
This lecture covers material similar to chapters 10 & 11 of Stallings. Computer Organisation & Architecture
  It covers the entirety of chapter 10
  It covers section 11.2 of chapter 11 up to two’ complement representations

## Slide 5: Overview
Number Systems
Integer Representations

## Slide 6: Number Systems

## Slide 7: Number Systems
Denary/Decimal or base ten - ten symbols
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9
Binary or base two - two symbols
  0, 1
Hexadecimal or base 16 - sixteen symbols
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Octal or base 8 - eight symbols
  0, 1, 2, 3, 4, 5, 6, 7.

## Slide 8: Why Binary?
On
True
Yes
Off
False
No

## Slide 9: Bits, Bytes and Words
Bit - binary digit
Byte - 8 bits
Word - 32 bits or 64 bits (in most systems).
The number of bits used to store numbers will determine the size of the numbers which can be stored and their precision.

## Slide 10: Positional notation: Base 10
527 = 5 102 + 2 101 + 7 100
 | 100’s place | 10’s place | 1’s place
Place | 102 | 101 | 100
Value | 100 | 10 | 1
Evaluate | 5 100 | 2 10 | 7 1
Sum | 500 | 20 | 7
 | 100’s place | 10’s place | 1’s place
Place | 102 | 101 | 100
Value | 100 | 10 | 1
Evaluate |  |  | 
Sum | 500 | 20 | 7

## Slide 11: Positional notation: Base 2
1101 01102 = 21410
Place | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Evaluate | 1 128 | 1 64 | 0 32 | 1 16 | 0 8 | 1 4 | 1 2 | 0 1
Sum | 128 | 64 | 0 | 16 | 0 | 4 | 2 | 0
Place | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Evaluate |  |  |  |  |  |  |  | 
Sum | 128 | 64 | 0 | 16 | 0 | 4 | 2 | 0

## Slide 12: Positional notation: Base B

## Slide 13: Range of possible numbers
where = range, = base, = number of digits.
Example
  = 102 = 100 different numbers (0 . . . 99)
Example
  = 216 = 65 536 or 64K (64 1024)
16-bit Program Counter can store 65 536 different numbers.

## Slide 14: Bit widths
Bits | Width
1 | 2 (0 and 1)
4 | 16 (0 to 15)
8 | 256
10 | 1024 (1K)
16 | 65536 (64K)
20 | 1 048 576 (1M)
32 | 4 294 967 296 (4G)

## Slide 15: Counting in base 2
Binary | 8’s (23) | 4’s (22) | 2’s (21) | 1’s (20) | Decimal
0 |  |  |  | 0 20 | 0
1 |  |  |  | 1 20 | 1
10 |  |  | 1 21 | 0 20 | 2
11 |  |  | 1 21 | 1 20 | 3
100 |  | 1 22 | 0 21 | 0 20 | 4
101 |  | 1 22 | 0 21 | 1 20 | 5
110 |  | 1 22 | 1 21 | 0 20 | 6
111 |  | 1 22 | 1 21 | 1 20 | 7
1000 | 1 23 | 0 22 | 0 21 | 0 20 | 8
Binary | 8’s (23) | 4’s (22) | 2’s (21) | 1’s (20) | Decimal
0 |  |  |  |  | 0
1 |  |  |  |  | 1
10 |  |  |  |  | 2
11 |  |  |  |  | 3
100 |  |  |  |  | 4
101 |  |  |  |  | 5
110 |  |  |  |  | 6
111 |  |  |  |  | 7
1000 |  |  |  |  | 8
Now You: Expand the table up to 15

## Slide 16: Binary Arithmetic
Example
  Compute (110 1101)2 + (1 0110)2.
1 | 1 | 1 | 1 | 1 |  |  | 
 | 1 | 1 | 0 | 1 | 1 | 0 | 1
 |  |  | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 |  |  | 
 | 1 | 1 | 0 | 1 | 1 | 0 | 1
 |  |  | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 17: Exercise: Binary Arithmetic
Now You:
Compute (1010)2 + (1110)2

## Slide 18: Binary Multiplication
Example
  Compute 11012 × 1012.
 |  |  | 1 | 1 | 0 | 1 | 
 |  |  |  | 1 | 0 | 1 | 
 | 1 | 1 | 1 |  |  |  | 
 |  |  | 1 | 1 | 0 | 1 | 1’s place
 |  |  |  |  | 0 |  | 2’s place
+ | 1 | 1 | 0 | 1 |  |  | 4’s place (bits left shifted twice)
1 | 0 | 0 | 0 | 0 | 0 | 1 | Result (sum)
 |  |  | 1 | 1 | 0 | 1 | 
 |  |  |  | 1 | 0 | 1 | 
 | 1 | 1 | 1 |  |  |  | 
 |  |  | 1 | 1 | 0 | 1 | 1’s place
 |  |  |  |  | 0 |  | 2’s place
+ | 1 | 1 | 0 | 1 |  |  | 4’s place (bits left shifted twice)
1 | 0 | 0 | 0 | 0 | 0 | 1 | Result (sum)

## Slide 19: Exercise: Binary Multiplication
Now You:
Compute (1010)2 (1110)2

## Slide 20: Converting decimal to binary
Algorithm, to convert decimal number to binary:
Divide by 2 to get
Remainder is the rightmost bit (least significant bit)
Divide by 2 to get
Remainder is the next rightmost bit
And so on, until
Divide by 2 to get 0
Remainder is the leftmost bit (most significant bit)

## Slide 21: Why does this work?
Therefore, each is a bit

## Slide 22: Example: converting decimal to binary
4210
42 / 2 = 21, remainder 0. Rightmost bit is 0.
21 / 2 = 10, remainder 1. Next rightmost bit is 1.
10 / 2 = 5, remainder 0. Next bit is 0.
5 / 2 = 2. remainder 1. Next bit is 1.
2 / 2 = 1, remainder 0. Next bit is 0.
1 / 2 = 0, remainder 1. Last bit is 1.
Put these in reverse order (because we go right to left) to get 1010102

## Slide 23: Example: alternative solution
Power | 6 | 5 | 4 | 3 | 2 | 1 | 0
Base 2 | 64 | 32 | 16 | 8 | 4 | 2 | 1
 |  | 1 | 0 | 1 | 0 | 1 | 0
Integer |  | 42 / 32 | 10 / 16 | 10 / 8 | 2 / 4 | 2 / 2 | 0 / 1
 |  | = 1 | = 0 | = 1 | = 0 | = 1 | = 0
Remainder |  | 10 | 10 | 2 | 2 | 0 | 0

## Slide 24: Exercise: converting decimal to binary
Now You: Convert 11510 to binary

## Slide 25: Converting decimal to hexadecimal
The same principal applies, except we divide by 16 rather than 2
Divide by 16 to get
Remainder is the rightmost digit
Divide by 16 to get
Remainder is the next rightmost digit
And so on, until
Divide by 16 to get 0
Remainder is the leftmost digit

## Slide 26: Example: converting decimal to hexadecimal
Show 803910 = 1F6716
Divide 8039 by 16 to get 502, remainder 7. Rightmost digit is 7.
Divide 502 by 16 to get 31, remainder 6. Next digit is 6.
Divide 31 by 16 to get 1, remainder 15. Next digit is F (15).
Divide 1 by 16 to get 0, remainder 1. Last digit is 1.
Reverse order to get 1F67.

## Slide 27: Exercise: converting decimal to hexadecimal
Now you: Convert 6526110 to hexadecimal

## Slide 28: Converting hexadecimal to binary
Converting between binary and hexadecimal is much easier
Remember that 4 bits give 16 possible values (24): 0 to 15.
  Hexadecimal has 16 digits representing 0 to 15
Hex to binary: Convert each hex digit to 4-bit binary and concatenate (from left to right)
Binary to hex: Split binary into groups of 4 bits (from right) and convert each group of 4 bits to a hex digit

## Slide 29: Example
1F6716 to binary
1 is 0001 as 4 binary digits
F(15) is 1111
6 is 0110
7 is 0111
Concatenated, from left to right, gives 0001 1111 0110 0111
Removing leading zeroes gives 1 1111 0110 01112.

## Slide 30: Example: converting hexadecimal to binary
Convert 11000000001110102 to hexadecimal
Split into groups of four bits: 1100 0000 0011 1010
Convert each group:
  1100 is C (12)
  0000 is 0
  0011 is 3
  1010 is A (10)
Hence, C03A16

## Slide 31: Exercise: converting hexadecimal to binary
Now You: Convert 78916 to binary

## Slide 32: Binary Fractions: Radix Point
Decimal point in base 10
Binary point in base 2
Some numbers cannot be represented (exactly) in some bases (with terminating, finite representations). Exact conversion may be impossible.

## Slide 33: Decimal Fractions
Move the number point one place to the right:
  Effect multiplies the number by the base number
  Example 139.010 → 139010
Move the number point one place to the left:
  Effect divides the number by the base number
  Example 139.010 → 13.910

## Slide 34: Binary Fractions
0.258910
Place |  | 10-1 | 10-2 | 10-3 | 10-4
Value |  | 1/10 | 1/100 | 1/1000 | 1/10000
Evaluate |  | 2 1/10 | 5 1/100 | 8 1/1000 | 9 1/10000
Result |  | 0.2 | 0.05 | 0.008 | 0.0009
Place |  | 10-1 | 10-2 | 10-3 | 10-4
Value |  | 1/10 | 1/100 | 1/1000 | 1/10000
Evaluate |  |  |  |  | 
Result |  | 0.2 | 0.05 | 0.008 | 0.0009
0.101012 = 0.6562510
Place |  | 2-1 | 2-2 | 2-3 | 2-4 | 2-5
Value |  |  |  |  |  | 
Evaluate |  |  |  |  |  | 
Result |  | 0.5 | 0 | 0.125 | 0 | 0.03125
Place |  | 2-1 | 2-2 | 2-3 | 2-4 | 2-5
Value |  |  |  |  |  | 
Evaluate |  |  |  |  |  | 
Result |  | 0.5 | 0 | 0.125 | 0 | 0.03125

## Slide 35: Binary and Decimal Fractions
There is no general relationship between fractions of types 1/10k and 1/2k.
Therefore, a number representable in base 10 may not be representable in base 2.
But the converse is true: all fractions of the form 1/2k can be represented in base 10.

## Slide 36: Converting decimal fractions to binary
Take the decimal fraction , where
Multiply by 2 to get , if , record 1 as first binary digit to right of point, if , record 0.
If , stop.
Otherwise, set to be if , or if
Multiply by 2 to get , if , record 1 as next binary digit to right of point, if , record 0.
If , stop.
Otherwise, set to be if or if
And so on, until

## Slide 37: Example
0.8110 = 0.1100112 (truncated to 6 binary places)
Check: 0.1100112 = 1 0.5 + 1 0.25 + 0 0.125 + 0 0.0625 + 1 0.03125 + 1 0.015625 = 0.79687510
Step | Fraction | Product | Bit
1 | 0.81 | 1.62 | 1
2 | 0.62 | 1.24 | 1
3 | 0.24 | 0.48 | 0
4 | 0.48 | 0.96 | 0
5 | 0.96 | 1.92 | 1
6 | 0.92 | 1.84 | 1

## Slide 38: Example
0.2510 = 0.012 (exactly)
Step | Fraction | Product | Bit
1 | 0.25 | 0.5 | 0
2 | 0.5 | 1.0 | 1

## Slide 39: Mixed number conversion
Integer and fractional parts must be converted separately
Radix point: fixed reference for the conversion
Digit to the left is a unit digit in every base
is always 1 regardless of the base .

## Slide 40: Exercise
Convert (8.375)10 to binary.
Convert (1.101)2 to decimal.

## Slide 41: Integer Representations

## Slide 42: Integer Representation
In the binary number system arbitrary numbers can be represented with:
  The digits zero and one
  The minus sign (for negative numbers)
  The period, or radix point (for numbers with a fractional component)
  For purposes of computer storage and processing we do not have the benefit of special symbols for the minus sign and radix point
  Only binary digits (0,1) may be used to represent numbers

## Slide 43: Unsigned Integer
An unsigned integer represent values from 0 to
number of bits for representation
Bits | Min value | Max
1 | 0 | 1
4 | 0 | 15
8 | 0 | 255
10 | 0 | 1023
16 | 0 | 65535
20 | 0 | 1 048 575
32 | 0 | 4 294 967 295

## Slide 44: Binary Coded Decimal
Complicated to do binary conversion to display numbers
Unsigned integer
Integers are stored as decimal numbers
  Sequence of binary encodings of decimal digits
Each decimal digit is stored as its 4-bit binary equivalent
E.g., 47810
  Convert 4, 7, & 8 to binary – 100, 111, 1000 respectively
  Prepend values less then 4 bits with zeroes, i.e. 0100, 0111, 1000
  Concatenate these values, i.e. 478 is represented as 0100 0111 1000

## Slide 45: Exercise
Convert 25110 to BCD

## Slide 46: Binary vs BCD
Decimal | Binary | BCD | 
68 | 0100 0100 | 0110 1000 | 
99 | 0110 0011 | 1001 1001 | Largest 8-bit BCD
255 | 1111 1111 | 0010 0101 0101 | Largest 8-bit binary

## Slide 47: Value range: binary vs BCD
No. of bits | BCD range | No. Decimal Digits | Binary range | No. Decimal Digits
4 | 0-9 | 1 | 0-15 | 2
8 | 0-99 | 2 | 0-255 | 3
12 | 0-999 | 3 | 0-4095 | 4
16 | 0-9999 | 4 | 0-65535 | 5
20 | 0-99 999 | 5 | 0-1 million | 7
24 | 0-999 999 | 6 | 0-16.8 million | 8
32 | 0-99 999 999 | 8 | 0-4.3 billion | 10
64 | 0-(1016 − 1) | 16 | 0-1.84 | 20
No. of bits | BCD range | No. Decimal Digits | Binary range | No. Decimal Digits
4 | 0-9 | 1 | 0-15 | 2
8 | 0-99 | 2 | 0-255 | 3
12 | 0-999 | 3 | 0-4095 | 4
16 | 0-9999 | 4 | 0-65535 | 5
20 | 0-99 999 | 5 | 0-1 million | 7
24 | 0-999 999 | 6 | 0-16.8 million | 8
32 | 0-99 999 999 | 8 | 0-4.3 billion | 10
64 | 0-(1016 − 1) | 16 |  | 20
Binary: 4 bits can hold 16 values (0 to 15)
BCD: 4 bits used to hold only 10 different values (0 to 9)

## Slide 48: Binary vs BCD
A binary representation is general preferred.
BCD for integers only used by certain business applications where input and output are more common than calculations

## Slide 49: Signed integer representation
Sign-magnitude representation
2’s complement

## Slide 50: Sign-magnitude
Left most bit is the sign bit
0 means positive
1 means negative
+18 = 00010010
−18 = 10010010
Problems:
  We need to consider both sign and magnitude in arithmetic
  Two representations of zero (+0 and −0)
Because of these drawbacks, sign-magnitude representation is rarely used in implementing the integer portion of the ALU

## Slide 51: Sign magnitude arithmetic
Addition
  Check sign bits: if both same then addition, different treat as subtraction
  Remove sign bits and add using standard binary arithmetic
  Sign bit is positive or negative depending on sign bits of operands
Subtraction
  Given operands &
  If
    Compute using standard binary arithmetic (remove sign bits)
  If
    Compute
    Negate result of

## Slide 52: Sign magnitude arithmetic
Multiplication
  Check if the two numbers have the same sign
  Remove the signs and multiply the numbers
  If the numbers had different signs originally, negate the answer.
Division
  Check if the two numbers have the same sign
  Remove the signs and divide the numbers
  If the numbers had different signs originally, negate the answer.

## Slide 53: Summary
Binary & Hexadecimal number systems
  Conversion
  Arithmetic
Representations of integers
  Unsigned integer
  BCD
  Sign-magnitude