## Slide 1
COMP1860: Building Our Digital World Computer Systems & Architecture
S1.W5.L2 Hardware Description Language
& Computer Aided Design LAB 2

## Slide 2
Learning Outcomes
Analyse and design a combinational logic circuit
Utilize a hardware simulator to design, test, and analyze the behavior of a digital circuit
Implement and debug combinational logic circuits using HDL

## Slide 3
Text Book
  Nand2Tetris HDL Guide / Documentation:
  The Elements of Computing Systems / Appendix 2: HDL

## Slide 4
Hardware Description Language
/**
* Xor gate.
*/
CHIP Xor {
IN a, b;
OUT out;
PARTS:
And (a=a, b=b, out=x);
Or (a=a, b=b, out=y);
Not (in=x, out=notx);
And (a=y, b=notx, out=out);
}
Header
Parts
  Nand2Tetris HDL Guide / Documentation:
  The Elements of Computing Systems / Appendix 2: HDL

## Slide 5
Introduced the Hardware Simulator
Simulate HDL chips
Automated test scripts
https://nand2tetris.github.io/web-ide/chip/

## Slide 6
Look at Solution for final problem from lab 1.5.1
Learn how to implement buses in HDL
Build some more of the chips for our Hack computer
Opportunity to start work on Activity sheet 1.6
Overview

## Slide 7
Two binary numbers, a and b, each of two digits, are represented as a1a­0 and b1b0 where a1, a0 and b1, b0 are Boolean variables which form the digits of the binary numbers.
Devise a combinatorial logic circuit, or circuits to provide outputs of X,Y, Z such that X=1 when a>b, Y=1 when a<b and Z=1 when a=b.
Implement the circuits in HDL. Create an appropriate test script and compare file to test your solution.
From last time

## Slide 8
 |  | a1a0 |  |  | 
 |  | 00 | 01 | 11 | 10
b1b0 | 00 | 0 | 1 | 1 | 1
 | 01 | 0 | 0 | 1 | 1
 | 11 | 0 | 0 | 0 | 0
 | 10 | 0 | 0 | 1 | 0
a1a0 | b1b0 | x
00 | 00 | 0
00 | 01 | 0
00 | 10 | 0
00 | 11 | 0
01 | 00 | 1
01 | 01 | 0
01 | 10 | 0
01 | 11 | 0
10 | 00 | 1
10 | 01 | 1
10 | 10 | 0
10 | 11 | 0
11 | 00 | 1
11 | 01 | 1
11 | 10 | 1
11 | 11 | 0

## Slide 9: Multi-bit bus
LSB = Least significant bit
MSB = Most significant bit
13
12
15
14
9
8
11
10
5
4
7
6
1
0
3
2
Example: 16-bit bus
0
0
1
0
0
0
1
0
0
1
1
1
0
1
1
1
In HDL sometimes we wish to manipulate a sequence of bits as a single entity
将一系列位作为一个整体来操作
In Nand2Tetris such a multi-bit entity is termed “bus”
16-bit bus：
把16个1bit的 输入/输出信号并联在一起，每1bit对应一个输入/输出信号
d c b a

## Slide 10: Working with buses: Example
/* Adds two 16-bit values. */
CHIP Adder {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/* Adds three 16-bit inputs. */
CHIP Adder3Way {
IN a[16], b[16], c[16];
OUT out[16];
out:
0
. . .
1
1
a:
1
0
1
15
. . .
. . .
1
1
b:
0
. . .
0
1
c:
1
. . .
0
0
[16] 代表16-bits bus

## Slide 11: Working with buses: Example
/* Adds two 16-bit values. */
CHIP Adder {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/* Adds three 16-bit inputs. */
CHIP Adder3Way {
IN a[16], b[16], c[16];
OUT out[16];
PARTS:
Adder(a=a , b=b, out=ab);
Adder(a=ab, b=c, out=out);
}
out:
0
. . .
1
1
a:
1
0
1
15
. . .
. . .
1
1
b:
0
. . .
0
1
c:
1
. . .
0
0
n-bit value (bus) can be treated as a single entity
Creates an internal bus pin (ab)
定义3个16-bits bus输入a, b, c；和1个16-bits输出out
16-bits数 a + b + c = out: a + b->ab ; ab + c -> out

## Slide 12: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0
回到题目，我们用a0a1和b0b1比较，输入用到了4个1bits信号，所以用一个16-bits的bus中的4bits就够了: a[4]
但是 and gate只要1-bit信号作为输入，
所以传入时，需要指定用4-bits信号中的哪一位作为输入，所以用下标指定（和数组一样a[1]）

## Slide 13: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* Bit-wise And of two 4-bit inputs */
CHIP And4 {
IN a[4], b[4];
OUT out[4];
PARTS:
And(a=a[0], b=b[0], out=out[0]);
And(a=a[1], b=b[1], out=out[1]);
And(a=a[2], b=b[2], out=out[2]);
And(a=a[3], b=b[3], out=out[3]);
}
Output bus pins can be subscripted
a:
1
0
1
3
2
1
0
0
b:
1
0
0
1
out:
1
0
0
0
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0
and01 = a[0] and a[1]
and02 = and01 and a[2]
out = and01 and and2
and01/02是芯片内引脚pin
out是芯片外引脚pin（1-bit）
out[0] = a[0] and b[0]
out[1] = a[1] and b[1]
out[2] = a[2] and b[2]
out[3] = a[3] and b[3]
out1-4是芯片外16-bits引脚pin的低4位

## Slide 14
将1-bit信号扩展到16-bits bus

## Slide 15: 信号切片
CHIP MyChip {
IN a[16], b[16];
OUT out[16];
PARTS:
And16(a=a, b=b, out=out, out[0..3]=lsb);
And4Way(a=lsb, out=4wayout);
}
Outputs only bus pins 0 to 7 as an internal bus called lsb of width 4.
Outputs the whole 16 bit bus
您还可以使用总线中的一系列位，而不是整个总线。
例如，如果您只想使用And16门输出中的4个最低有效位，或者只想使用16位计数器或寄存器的8位。

## Slide 16: 信号切片
CHIP MyChip {
IN input1[16], input2[16];
OUT output[16];
PARTS:
And16(a=input1, b=true, out=output);
And16(a[0..7]=false, a[8..15]=input1[8..15], out=output);
}
将a的8个最低有效位设置为false，将输入1的8个最高有效位设置成最高有效位。
Sets all 16 bits of input b to true.
You can manually set pins, buses or parts of buses to high (true) or low (false) values. This can be useful for masking bits.
You can also connect different sources to different parts of a bus.

## Slide 17
Your Turn: And16
out = 0 0 1 0 1 0 0 1 0 0 0 0 1 0 0 0
a = 1 0 1 0 1 0 1 1 0 1 0 1 1 1 0 0
b = 0 0 1 0 1 1 0 1 0 0 1 0 1 0 1 0
CHIP And16 {
IN a[16], b[16];
OUT out[16];
PARTS:
// Put your code here:
}
Implementation tip
A straightforward 16-bit extension of the elementary And gate
(See notes about working with multi-bit buses).
Example:

## Slide 18
Your turn: Implement a 2-Way 1-bit multiplexer (MUX)
CHIP Mux {
IN a, b, sel;
OUT out;
PARTS:
// Put your code here:
}
Mux.hdl
Your saw Multiplexers in lecture 1.4.1
A multiplexer is a selector
One of the inputs will be output
Which one depends on the selection input (sel)
The preamble for the chip is:
sel | out
0 | a
1 | b
a
b
sel
out
Mux

## Slide 19
Your turn: Implement a 2-Way 16-bit multiplexer
CHIP Mux16 {
IN a[16], b[16], sel;
OUT out[16];
PARTS:
// Put your code here:
}
Mux16.hdl
In our computer we are likely to want to select between 16-values rather than 1-bit values.
Create a new chip Mux16 that selects between 16-bit input values and outputs a 16-bit output.
The Nand2Tetris built in chips provides the following chips that you might find helpful:
Not16(in,out) a 16-bit wide Not gate.
Or16(a,b,out) a 16-bit wide Or Gate.

## Slide 20
Your turn: Implement a 16-bit, 4-way multiplexer
sel[1] | sel[0] | out
0 | 0 | a
0 | 1 | b
1 | 0 | c
1 | 1 | d
Implementation tip:
We can use a 2-bit bus for the selection bits to provide 4 possible values for sel..
The chip can be built from several Mux16 gates.
CHIP Mux4Way16 {
IN a[16], b[16], c[16], d[16],
sel[2];
OUT out[16];
PARTS:
// Put your code here:
}
Mux4Way16.hdl
As you saw in lecture 1.4.1 you can also build multiplexers that select between more than 2 inputs.
On the right is an example of a 4-way (4-to-1) Multiplexer.

## Slide 21
Your turn: Implement a 2-way demultiplexer (DMUX)
sel | Use output
0 | a
1 | b
CHIP DMux {
IN in, sel;
OUT a, b;
PARTS:
// Put your code here:
}
DMux.hdl
As you saw in lecture 1.4.1 Demultiplexers work the other way. They select the output path
The sel input determines which output line (a or b) the input (in) is sent to.
in
a
b
sel

## Slide 22
Your turn: A 4-way demultiplexer
sel[1] | sel[0] | out
0 | 0 | a
0 | 1 | b
1 | 0 | c
1 | 1 | d
Implementation tip:
The chip can be built from several DMux gates.
CHIP DMux4Way {
IN in, sel[2];
OUT a, b, c, d;
PARTS:
// Put your code here:
}
DMux4Way.hdl
We can expand this to have as many outputs as we wish.
We can use a bus for the selection bits to provide all possible values for sel.
in
b
c
sel
a
d

## Slide 23
Now have a go at Activity Sheet 1.5
  Request the activity sheet using the link in Minerva (question 2 is part of your portfolio)
  You should upload the tst files obtained from the activity sheet to your repository to help you test your solutions to question 2.
  Once you have a working solution for question 2, submit your solution to Gradescope to see if it passes all the tests. You can do this by uploading your A6Q2.hdl file.
Your turn

## Slide 24
Your turn:
Given: Nand
Goal: Build the following gates:
Elementary logic gates
Not
And
Or
Xor
Mux
DMux
Or8Way
Mux4Way16
Mux8Way16
DMux4Way
DMux8Way
Multi-way variants
Not16
And16
Or16
Mux16
16-bit variants
If you wish to finish building some other gates we will use then complete the list below

## Slide 25
Learnt how to implement buses in HDL
Started to build the chips we will need for our Hack computer
And16
Mux
                Mux16
                Mux4Way16
Summary